UEA Contribution 2 to D12

Modelling Indices of European extreme rainfall and temperature using inter-annual variability of large-scale circulation

Malcolm Haylock, UEA

# Introduction

This document discusses the application of a downscaling technique developed for UK extreme rainfall to Europe-wide temperature and rainfall. A full description of the downscaling technique can be found in the primary UEA contribution to D12.

# Data

## Predictands

Daily temperature and rainfall was analysed for all stations from version 2 of the STARDEX European data set, with the addition of 10 Italian stations. 13 climate indices were calculated:

pav	Mean daily rainfall

pq90	90th percentile of rainday amounts (mm/day)

px5d	Greatest 5-day total rainfall

pint	Simple Daily Intensity (rain per rainday)

pxcdd	Max no. consecutive dry days

pfl90	% of total rainfall from events > long-term P90

pnl90	No. of events > long-term 90th percentile of raindays

txav	Mean Tmax

tnav	Mean Tmin

txq90	90th percentile of Tmax

tnq10	10th percentile of Tmin

tnfd	No of frost days

Txhw90	percentile based heat wave duration

## Predictors

The best predictor set was chosen from four possible predictors: MSLP, relative humidity at 700hPa, specific humidity at 700hPa and temperature at 700hPa. The best predictor set was chosen for each index and season using cross-validation during the training period (see primary contribution).

# Results

Figure 1 shows the Spearman correlation for downscaled and observed indices during hindcast period averaged across all stations. The temperature indices are much better downscaled the rainfall indices, which all have correlations less than 0.4. In general DJF shows the highest correlations followed by MAM. As for the UK results, the best-reproduced extreme rainfall indices are pxcdd and pnl90.

Figure 1: Spearman rank correlation for downscaled and observed indices during hindcast period averaged across all stations.

The patterns of hindcast correlations were plotted for each index and season showing that in most cases the correlations are regionally coherent. For example, Figure 2 shows the correlations for txq90 for SON. While central and southwest Europe has correlations up to 0.77, the SE and NW part of the region contains mainly negative correlations. Figure 3 shows a similar figure for pnl90 for MAM. While the pattern is less coherent than for Fig. 2, there is still some degree of regionalisation.

The fact that there are large areas of negative correlations suggests that the entire European region is probably too heterogeneous to be included in a single CCA analysis. Therefore an analysis that divides the data into more coherent regions is necessary.

Figure 2: Spearman correlation for hindcast txq90 for SON. Red circles indicate +ve correlations and blue indicates –ve.  The diameter of the circle is proportional to magnitude of the correlation.

Figure 3: Spearman correlation for hindcast pnl90 for MAM. Red circles indicate +ve correlations and blue indicates –ve.  The diameter of the circle is proportional to magnitude of the correlation.